## Slide 1: AI-POWERED LANDSLIDE REGION MAPPING USING SEMANTIC SEGMENTATION
Suraj Karki
04.09.2025
Dr.-Ing. Constanze Schwan
Notes: HAW

## Slide 2
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 2
Introduction
Landslides are one of the most common and dangerous natural disasters globally.
It causes significant damage to infrastructure, agriculture, and human life.
According to the UNDRR, over 4,000 people die each year globally due to landslides. 1
Rapid post-disaster mapping is vital for guiding rescue efforts and risk assessment.
1. UNDRR, Human Cost of Disasters: An Overview of the Last 20 Years (2000–2019), United Nations Office for Disaster Risk Reduction, 2020. [Online]. Available: https://www.undrr.org/publication/human-cost-disasters-overview-last-20-years-2000-2019
Notes: HAW

## Slide 3
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 3
Problem statement
Manual mapping of landslide areas in post landslide assessment is slow, inconsistent, and risky.
Precise, up-to-date landslide masks are needed for:
  Damage assessment
  Recovery planning
  Updating geohazards maps
A system is required to automatically generate post-landslide maps.
Notes: HAW

## Slide 4
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 4
objective
To develop a deep learning model for precise landslide mapping
To obtain high performance in segmenting landslide regions from satellite and UAV imagery
To enable real-time monitoring and support disaster management efforts
Figure Source: Zhao et al. (2023), A global dataset of landslide inventories compiled from satellite imagery. Scientific Data. https://doi.org/10.1038/s41597-023-02847-z
Notes: HAW

## Slide 5
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 5
State of the art
Landslide Detection and Segmentation using Remote Sensing Images and Deep Neural Network 2
  Dataset: Landslide4Sense (128x128 pixels;14 channels)
  Approaches:
    Enhanced U-net structure with residual-convolutional layers
    Custom multi-head attention layer (Pro-Att) to focus on landslide regions
    Multi-resolution segmentation outputs: at 64×64, 128×128, and 256×256 (ensembled)
    Generate 12 additional bands to improve input data
    Combined focal loss and IoU loss as loss function (handle class imbalance)
  It achieved an mIoU of 76.07 and F1-score of 84.07, surpassing the baseline.
2. C. Le, L. Pham, J. Lampert, M. Schlögl, and A. Schindler, “Landslide detection and segmentation using remote sensing images and deep neural network,” arXiv preprint arXiv:2312.16717, 2023. [Online]. Available: https://arxiv.org/abs/2312.16717
Notes: HAW

## Slide 6
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 6
State of the art
LandslideSegNet: an effective deep learning network for landslide segmentation using remote sensing imagery 3
  Dataset: Landslide4Sense Modified (256x256;3 channels)
  Approaches:
    Proposed LandslideSegNet, a custom architecture for landslide segmentation.
    It contains Encoder-decoder Residual Block, enhances feature extraction by combining local and contextual information.
    And, Hybrid Attentional Atrous Convolution Module improves efficiency by focusing on critical features and suppressing irrelevant information.
3. Şener, A., Ergen, B. LandslideSegNet: an effective deep learning network for landslide segmentation using remote sensing imagery. Earth Sci Inform 17, 3963–3977 (2024). https://doi.org/10.1007/s12145-024-01434-z
Notes: HAW

## Slide 7
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 7
State of the art
LandslideSegNet: an effective deep learning network for landslide segmentation using remote sensing imagery 3
  It achieved an mIoU of 73.65 and precision of 71.48.
3. Şener, A., Ergen, B. LandslideSegNet: an effective deep learning network for landslide segmentation using remote sensing imagery. Earth Sci Inform 17, 3963–3977 (2024). https://doi.org/10.1007/s12145-024-01434-z
Notes: HAW

## Slide 8
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 8
State of the art
A landslide area segmentation method based on an improved UNet 4
  Dataset: Bijie Landslide Dataset (3 channels, 770 landslide images and 2003 non-landslide)
  Approaches:
    Enhanced U-net structure with dilated convolution and EMA attention.
    Dilated convolution enlarges the receptive field and capture richer contextual information.
    EMA attention helps with multi-scale feature extraction.
    The proposed Pag module(skip conn.) enhances multi-scale feature fusion, improving transmission and reducing pixel information loss caused when resolution changes in U-Net.
  It achieved an mIoU of 83.85 and precision of 80.26.
4. Li, G., Li, K., Zhang, G. et al. A landslide area segmentation method based on an improved UNet. Sci Rep 15, 11852 (2025). https://doi.org/10.1038/s41598-025-94039-5
Notes: HAW

## Slide 9
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 9
State of the art
TransLandSeg: A Transfer Learning Approach for Landslide Semantic Segmentation Based on Vision Foundation Model 5
  Dataset: Bijie Landslide Dataset and Landslide4Sense
  Approaches:
    Proposed a custom architecture, based on Segment Anything Model (SAM).
    Applies Adaptive Transfer Learning (ATL) to adapt SAM’s segmentation capabilities for landslide semantic segmentation.
    Image Encoder and Mask Decoder
    ATL fine-tuning layer inserted between Transformer blocks that learns landslide-specific features.
5. C. Hou et al., "A Transfer Learning Approach for Landslide Semantic Segmentation Based on Visual Foundation Model," in IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 18, pp. 11561-11572, 2025, doi: 10.1109/JSTARS.2025.3559884.
Notes: HAW

## Slide 10
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 10
State of the art
TransLandSeg: A Transfer Learning Approach for Landslide Semantic Segmentation Based on Vision Foundation Model 5
  It achieved an mIoU of 88.10 and precision of 93.14 on bijie dataset.
  It achieved an mIoU of 75.99 and precision of 84.99 on landslide4sense dataset.
5. C. Hou et al., "A Transfer Learning Approach for Landslide Semantic Segmentation Based on Visual Foundation Model," in IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 18, pp. 11561-11572, 2025, doi: 10.1109/JSTARS.2025.3559884.
Notes: HAW

## Slide 11
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 11
workflow
General steps include: data collection, pre-processing, model training, testing, and deployment.
The overall workflow of the project is illustrated in the figure below.
Notes: HAW

## Slide 12
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 12
Data acquisition
Landslide4Sense Dataset 6
  Source: Institute of Advanced Research in Artificial Intelligence (IARAI)
  Regions: Collected from four regions (Iburi, Kodagu, Rasuwa, Taitung)
  Include earthquake and rainfall triggers landslide
  Satellite: Sentinel-2
  Topographic: ALOS (Advanced Land Observing Satellite
  Acquisition Process: Data aggregated from public satellite archives
  Annotation Process: annotations via Object-Based Image Analysis (OBIA)
6. O. Ghorbanzadeh et al., "Landslide4Sense: Reference benchmark data and deep learning models for landslide detection," IEEE Trans. Geosci. Remote Sens., vol. 60, pp. 1–17, 2022, doi: 10.1109/TGRS.2022.3215209.
Notes: HAW

## Slide 13
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 13
Data acquisition
Landslide4Sense Dataset 6
  Geolocations of the selected case study areas shown on the global landslide susceptibility map.
6. O. Ghorbanzadeh et al., "Landslide4Sense: Reference benchmark data and deep learning models for landslide detection," IEEE Trans. Geosci. Remote Sens., vol. 60, pp. 1–17, 2022, doi: 10.1109/TGRS.2022.3215209.
Notes: HAW

## Slide 14
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 14
Data acquisition
CAS Landslide Dataset 7
  Source: Institute of Mountain Hazards and Environment, Chinese Academy of Sciences.
  Regions: Collected from nine diverse region
  Include earthquake and rainfall triggers landslide
  Satellite: Sentinel-2, Landsat, WorldView2/3, Planet, SuperView-1, GF-1
  UAV: High-resolution imagery from Sichuan Geomatics Center and partners.
  Acquisition Process: Satellite data sourced via Google Earth Engine, Digital Globe, and authorized providers; UAV data collected through drone.
7. Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Notes: HAW

## Slide 15
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 15
Data acquisition
Annotation Process
  Pixel-level annotations created using QGIS and LabelMe.
  guided by landslide inventories, verified by geologists, cross-checked by team
Figure Source: Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Notes: HAW

## Slide 16
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 16
Data structure
Landslide4Sense Dataset
  Total Input: 3,799 images (128x128 pixels, 14 channels).
  Channels: 12 Sentinel-2 bands (B1–B12), ALOS PALSAR slope (B13), DEM (B14).
  Output: 128x128x1 binary mask
  Split:
    Training: 3,799, Validation: 245, Testing: 800
  Distribution:
    Train Set: 2,231 landslide, 1,568 non-landslide;
    Valid Set: 146 landslide, 99 non-landslide;
    Test Set: Test: 536 landslide, 264 non-landslide.
Notes: HAW

## Slide 17
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 17
Data structure
Bands
Notes: HAW

## Slide 18
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 18
Data structure
Landslide4Sense Dataset
  Band Statistics:
Notes: HAW

## Slide 19
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 19
Data structure
CAS Landslide Dataset
  Set 1: UAV
    Total Inputs: 10,939 images (512x512 pixels, 3 channels)
    Channels: RGB
    Output: 512x512x1 binary mask
    Split:
      Training: 8,753, Validation: 1093, Testing: 1093
    Distribution: All images have landslide region
Notes: HAW

## Slide 20
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 20
Data structure
CAS Landslide Dataset
  Set 2: Satellite
    Total Inputs: 7,422 images (512x512 pixels, 3 channels)
    Channels: RGB
    Output: 512x512x1 binary mask
    Split:
      Training: 5,938, Validation: 742, Testing: 742
    Distribution: All images have landslide region
Notes: HAW

## Slide 21
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 21
Data structure
Detailed Information on CAS Landslide Dataset (UAV set)
Subdataset | Amount | Acquisition Time | Source | Sensor | Ground Resolution (m)
Moxitaidi | 984 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 0.6
Moxitaidi | 483 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 1
Moxi Town | 1635 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 0.2
Moxi Town | 160 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 1
Longxi River | 2504 | 2011.03–2011.05 | Sichuan Geomatics Center | UAV | 0.5
Jiuzhai Valley | 5925 | 2017.08–2017.09 | Sichuan Geomatics Center | UAV | 0.2
Jiuzhai Valley | 1752 | 2017.08–2017.09 | Sichuan Geomatics Center | UAV | 0.5
Notes: HAW

## Slide 22
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 22
Data structure
Detailed Information on CAS Landslide Dataset (Satellite set)
Subdataset | Amount | Acquisition Time | Source | Sensor | Ground Resolution (m)
Palu | 817 | 2021.01–2021.11 | Digital Globe Open Data Program | WorldView2/3 | 5
Lombok | 436 | 2019.05–2019.12 | Digital Globe Open Data Program | WorldView2/3 | 5
Hokkaido Iburi-Tobu | 1484 | 2018.09–2018.10 | Geospatial Information Authority of Japan | SAT | 3
Tiburon Peninsula (Sentinel) | 606 | 2020.03–2020.06 | European Space Agency | Sentinel-2/L2A | 5
Tiburon Peninsula (Planet) | 325 | 2021.09–2021.12 | Planet | Planet | 4
Mengdong | 1155 | 2018.11.04 | Beijing Lanyu Fangyuan Technology Co., Ltd. | SuperView-1 | 0.5
Moxitaidi (SAT) | 652 | 2022.09–2022.10 | European Space Agency | Sentinel-2/L2A | 0.6
Longxi River (SAT) | 1769 | 2015.03–2015.12 | China Centre for Resources Satellite Data and Application | GF-1 | 0.5
Wenchuan | 178 | 2008.11–2008.12 | U.S. Geological Survey | Landsat | 5
Notes: HAW

## Slide 23
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 23
Data structure
Figure Source: Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Images and Labels of Samples from the Subdatasets of the CAS Landslide Dataset.
Notes: HAW

## Slide 24
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 24
ML models
1. Unet
  A FCN originally designed for biomedical image segmentation.
  Widely used in remote sensing for image classification and
  object detection, including landslide detection.
  Encoder: Captures low-level features
  Decoder: Captures high-level features and reconstructs image
  Skip Connections: preserve fine-grained details and improve
  accuracy.
Source: O. Ronneberger, P. Fischer, and T. Brox, “U-Net: Convolutional networks for biomedical image segmentation,” in Proc. Int. Conf. Med.
Image Comput.-Assist. Intervent. Cham, Switzerland: Springer, 2015, pp. 234–241.
Notes: HAW

## Slide 25
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 25
ML models
2. Unet++
  An improved version of U-Net.
  redesigned skip pathways (shown in green): bridges the
  semantic gap between encoder and decoder
  dense skip connections (shown in blue)
  deep supervision (shown in red): allows pruning to trade off speed and accuracy by using multiple output branches.
  Enhances feature fusion for improved accuracy and gradient flow.
Source: https://jinglescode.github.io/2019/12/02/biomedical-image-segmentation-u-net-nested/
Notes: HAW

## Slide 26
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 26
ML models
3. PSPNet
  Uses pyramid pooling to learn global context information.
  Applies regional aggregation to capture multi-scale
  features.
  Fuses features from four different pyramid scales
  Achieves effective multi-scale feature learning
  Can able to efficiently work with variable size objects of the image
Source: H. Zhao, J. Shi, X. Qi, X. Wang and J. Jia, "Pyramid Scene Parsing Network," 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR), Honolulu, HI, USA, 2017, pp. 6230-6239, doi: 10.1109/CVPR.2017.660.
Notes: HAW

## Slide 27
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 27
ML models
4. FPN
  Designed for multi-scale segmentation
  Builds a top-down feature pyramid from deep to shallow
  layers
  Combines low-resolution semantic-rich features
  with high-resolution spatial-rich features
  Enhances segmentation of small, medium, and large objects
Source: Wangiyana, Sandhi & Samczynski, Piotr & Gromek, Artur. (2022). Data Augmentation for Building Footprint Segmentation in SAR Images: An Empirical Study. Remote Sensing. 14. 2012. 10.3390/rs14092012.
Notes: HAW

## Slide 28
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 28
ML models
5. MANet
  Focuses on fine-grained semantic segmentation
  Utilizes multi-scale feature extraction for diverse
  object sizes
  Incorporates attention mechanisms to highlight
  important regions
  Enhances boundary details and small object recognition
  Suitable for complex and cluttered scenes like satellite images
Source: R. Li, S. Zheng, C. Zhang, C. Duan, J. Su, L. Wang, and P. M. Atkinson, “Multiattention Network for Semantic Segmentation of Fine-Resolution Remote Sensing Images,” IEEE Transactions on Geoscience and Remote Sensing, vol. 60, pp. 1–13, 2022, doi: 10.1109/TGRS.2021.3093977.
Notes: HAW

## Slide 29
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 29
ML models
6. Segformer
  Transformer-based architecture for semantic segmentation
  Hierarchical Transformer encoder: extract coarse
  and fine features
  Lightweight MLP decoder: directly fuse these multi-level
  features and predict the semantic segmentation mask
  Achieves strong accuracy–efficiency trade-off for high-resolution images
  FFN: Feed-forward Network
Source: E. Xie, W. Wang, Z. Yu, A. Anandkumar, J. M. Alvarez, and P. Luo, “SegFormer: Simple and Efficient Design for Semantic Segmentation with Transformers,” arXiv preprint arXiv:2105.15203, 2021. [Online]. Available: https://arxiv.org/abs/2105.15203
Notes: HAW

## Slide 30
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 30
fine-tuning
Fine-tuning is decided based on the available hardware resources, datasets, and project timeframe
Approach:
  Used pre-trained encoders: by freezing the encoder weights (imagenet)
    Resnet 18, Resnet34, Resnet50
    Mobilenet V2
    Densenet 161
    Efficientnet-b2
    Xception
  Decoder part of the model is fine-tuned
Notes: HAW

## Slide 31
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 31
fine-tuning
Experimental Setup
  Hardware:
    DA-Cluster: 8 CUDA-capable GPUs (NVIDIA Tesla P100, each with 12 GB)
  Software:
    Segmentation Models: Pytorch based library to build and train segmentatinon models
    Streamlit: Python library to build interactive web apps
Notes: HAW

## Slide 32
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 32
fine-tuning
Experimental Setup
  Hyperparameters:
    Batch Size: 8, 32
    Learning Rate: 0.001 (Adam optimizer, LRscheduler: Cosine Annealing )
    Number of Epochs: 300
    Loss Function: Focal Loss
    Early Stopping to avoid overfitting
  Complete code for training, evaluation, and deployment is available in the following GitHub repository:
    https://github.com/surajkarki66/AI-Powered_Landslide_Region_Mapping_using_Semantic_Segmentation
Notes: HAW

## Slide 33
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 33
Training Results – landslide4sense dataset
Dataset and Per Image IoU of Unet with MobilenetV2 encoder, which is best performing model
Notes: HAW

## Slide 34
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 34
Training Results – landslide4sense dataset
Precision and recall of Unet with MobilenetV2 encoder, which is best performing model
Notes: HAW

## Slide 35
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 35
Evaluation Results – landslide4sense dataset
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
FPN | MobileNet | 0.4419 | 0.4041 | 0.5756 | 0.9878 | 0.6212 | 0.6560
 | ResNet18 | 0.4321 | 0.4141 | 0.5857 | 0.9873 | 0.6349 | 0.6214
 | ResNet50 | 0.3906 | 0.3258 | 0.4915 | 0.9861 | 0.5522 | 0.6029
 | Xception | 0.3960 | 0.3122 | 0.4758 | 0.9857 | 0.6098 | 0.5842
MANet | Xception | 0.3934 | 0.3784 | 0.5490 | 0.9866 | 0.6159 | 0.6037
 | EfficientNet-B2 | 0.3451 | 0.3542 | 0.5231 | 0.9850 | 0.6267 | 0.5389
 | MobileNetV2 | 0.4232 | 0.4283 | 0.5998 | 0.9834 | 0.6796 | 0.6256
 | ResNet50 | 0.3319 | 0.3739 | 0.5443 | 0.9841 | 0.6928 | 0.5077
PSPNet | EfficientNet-B2 | 0.3855 | 0.3956 | 0.5669 | 0.9841 | 0.6219 | 0.5840
 | MobileNetV2 | 0.3896 | 0.3717 | 0.5419 | 0.9861 | 0.5940 | 0.5794
 | ResNet50 | 0.4074 | 0.3934 | 0.5646 | 0.9831 | 0.5971 | 0.6370
 | Xception | 0.3744 | 0.3541 | 0.5230 | 0.9862 | 0.5617 | 0.5930
 | DenseNet161 | 0.3974 | 0.4205 | 0.5920 | 0.9841 | 0.6042 | 0.6663
Segformer | ResNet18 | 0.4272 | 0.4132 | 0.5847 | 0.9873 | 0.6399 | 0.6226
 | ResNet34 | 0.4305 | 0.4120 | 0.5835 | 0.9845 | 0.6817 | 0.5924
UNet | DenseNet161 | 0.3192 | 0.4019 | 0.5734 | 0.9810 | 0.7495 | 0.4971
 | MobileNetV2 | 0.4444 | 0.4258 | 0.5973 | 0.9874 | 0.6996 | 0.6176
 | ResNet50 | 0.3619 | 0.4028 | 0.5743 | 0.9851 | 0.7218 | 0.5338
 | Xception | 0.4459 | 0.3536 | 0.5225 | 0.9814 | 0.6824 | 0.5856
UNet++ | MobileNetV2 | 0.4373 | 0.4018 | 0.5733 | 0.9875 | 0.6295 | 0.6423
 | Xception | 0.3149 | 0.3505 | 0.5191 | 0.9813 | 0.7496 | 0.4440
 | ResNet50 | 0.4215 | 0.3941 | 0.5654 | 0.9833 | 0.6272 | 0.6445
 | EfficientNet-B2 | 0.3659 | 0.4173 | 0.5888 | 0.9840 | 0.7141 | 0.5721
Notes: HAW

## Slide 36
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 36
Evaluation Results – landslide4sense dataset
Best Performing Models (Top-2) on Landslide4Sense Dataset
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet | MobileNetV2 | 0.4444 | 0.4258 | 0.5973 | 0.9874 | 0.6996 | 0.6176
UNet | Xception | 0.4459 | 0.3536 | 0.5225 | 0.9814 | 0.6824 | 0.5856
10 Fold Cross Validation Result
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet | MobileNetV2 | 0.5898 | 0.5580 | 0.7208 | 0.9880 | 0.7248 | 0.7870
Due to large number of experiments; detailed results available at the link below.
  https://drive.google.com/drive/folders/1kx3PE8OjQAdeSY55L-80fjDuaGewYr5C?usp=sharing
Notes: HAW

## Slide 37
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 37
Sample predictions – landslide4sense dataset
Notes: HAW

## Slide 38
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 38
Training Results – CAS Landslide dataset (UAV)
Dataset and Per Image IoU of Unet++ with ResNet50 encoder, which is best performing model
Notes: HAW

## Slide 39
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 39
Training Results – CAS Landslide dataset (UAV)
Precision and recall of Unet++ with ResNet50 encoder, which is best performing model
Notes: HAW

## Slide 40
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 40
Evaluation Results – CAS Landslide dataset (UAV)
Architecture | Backbone | Per-image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
FPN | MobileNet | 0.7986 | 0.9181 | 0.9573 | 0.9844 | 0.8606 | 0.9643
 | ResNet18 | 0.9002 | 0.9617 | 0.9805 | 0.9931 | 0.9386 | 0.9818
 | ResNet50 | 0.8895 | 0.9589 | 0.9790 | 0.9923 | 0.9237 | 0.9835
 | Xception | 0.9153 | 0.9720 | 0.9858 | 0.9950 | 0.9382 | 0.9882
MANet | Xception | 0.8171 | 0.9274 | 0.9623 | 0.9865 | 0.8359 | 0.9906
 | EfficientNet-B2 | 0.8628 | 0.9491 | 0.9739 | 0.9905 | 0.8930 | 0.9848
 | MobileNetV2 | 0.5350 | 0.6976 | 0.8218 | 0.9374 | 0.6456 | 0.8652
 | ResNet50 | 0.8842 | 0.9597 | 0.9795 | 0.9924 | 0.9199 | 0.9820
PSPNet | EfficientNet-B2 | 0.7487 | 0.8811 | 0.9368 | 0.9769 | 0.8499 | 0.9271
 | MobileNetV2 | 0.8230 | 0.9310 | 0.9643 | 0.9870 | 0.8583 | 0.9763
 | ResNet50 | 0.8105 | 0.9223 | 0.9596 | 0.9855 | 0.8645 | 0.9660
 | Xception | 0.7600 | 0.8916 | 0.9427 | 0.9782 | 0.8890 | 0.9163
Segformer | MobileNetV2 | 0.7387 | 0.8981 | 0.9463 | 0.9806 | 0.7845 | 0.9671
 | ResNet18 | 0.9042 | 0.9613 | 0.9803 | 0.9929 | 0.9453 | 0.9799
 | ResNet34 | 0.9140 | 0.9653 | 0.9823 | 0.9937 | 0.9372 | 0.9893
 | ResNet50 | 0.7020 | 0.8890 | 0.9412 | 0.9794 | 0.7085 | 0.9953
UNet | DenseNet161 | 0.8661 | 0.9485 | 0.9736 | 0.9903 | 0.9132 | 0.9794
 | MobileNetV2 | 0.8178 | 0.9274 | 0.9624 | 0.9862 | 0.8725 | 0.9707
 | ResNet50 | 0.9346 | 0.9732 | 0.9864 | 0.9951 | 0.9578 | 0.9888
 | Xception | 0.9290 | 0.9735 | 0.9866 | 0.9952 | 0.9468 | 0.9899
UNet++ | EfficientNet-B2 | 0.8592 | 0.9454 | 0.9719 | 0.9897 | 0.9022 | 0.9816
 | MobileNetV2 | 0.8181 | 0.9266 | 0.9619 | 0.9862 | 0.8642 | 0.9777
 | ResNet18 | 0.8981 | 0.9582 | 0.9787 | 0.9925 | 0.9298 | 0.9842
 | ResNet50 | 0.9519 | 0.9816 | 0.9907 | 0.9966 | 0.9676 | 0.9919
Notes: HAW

## Slide 41
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 41
Evaluation Results – CAS Landslide dataset (UAV)
Best Performing Models (Top-2) on CAS Landslide Dataset (UAV Version)
Architecture | Backbone | Per-image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet++ | ResNet50 | 0.9519 | 0.9816 | 0.9907 | 0.9966 | 0.9676 | 0.9919
UNet | ResNet50 | 0.9346 | 0.9732 | 0.9864 | 0.9951 | 0.9578 | 0.9888
5 Fold Cross Validation Result
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet++ | ResNet50 | 0.9456 | 0.9786 | 0.9893 | 0.9962 | 0.9654 | 0.9908
Due to large number of experiments; detailed results available at the link below.
  https://drive.google.com/drive/folders/14RgcVSGZQITB6Kr225ZBBL_kVOwUb_L7?usp=sharing
Notes: HAW

## Slide 42
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 42
Sample predictions– CAS Landslide dataset (UAV)
Notes: HAW

## Slide 43
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 43
Training Results – CAS Landslide dataset (Satellite)
Dataset and Per Image IoU of Unet with DenseNet161 encoder, which is best performing model
Notes: HAW

## Slide 44
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 44
Training Results – CAS Landslide dataset (satellite)
Precision and recall of Unet with DenseNet161 encoder, which is best performing model
Notes: HAW

## Slide 45
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 45
Evaluation Results – CAS Landslide dataset (Satellite)
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
FPN | MobileNet | 0.6485 | 0.7968 | 0.8869 | 0.9813 | 0.7609 | 0.8892
 | ResNet18 | 0.7858 | 0.8609 | 0.9253 | 0.9889 | 0.8618 | 0.9293
 | ResNet50 | 0.8004 | 0.9023 | 0.9486 | 0.9915 | 0.8699 | 0.9511
 | Xception | 0.8366 | 0.9065 | 0.9509 | 0.9928 | 0.8801 | 0.9658
MANet | Xception | 0.8108 | 0.8830 | 0.9379 | 0.9909 | 0.8619 | 0.9566
 | EfficientNet-B2 | 0.7721 | 0.8645 | 0.9273 | 0.9892 | 0.8554 | 0.9259
 | MobileNetV2 | 0.7233 | 0.8412 | 0.9138 | 0.9866 | 0.8046 | 0.9258
 | ResNet50 | 0.7958 | 0.8781 | 0.9351 | 0.9905 | 0.8542 | 0.9495
PSPNet | EfficientNet-B2 | 0.5845 | 0.7234 | 0.8395 | 0.9776 | 0.6455 | 0.9008
 | MobileNetV2 | 0.5379 | 0.6757 | 0.8065 | 0.9712 | 0.6553 | 0.8060
 | ResNet50 | 0.6999 | 0.8291 | 0.9066 | 0.9855 | 0.7697 | 0.9194
 | Xception | 0.5555 | 0.6711 | 0.8032 | 0.9657 | 0.8729 | 0.7011
 | DenseNet161 | 0.6887 | 0.8285 | 0.9062 | 0.9845 | 0.7802 | 0.9077
Segformer | MobileNetV2 | 0.7326 | 0.8446 | 0.9157 | 0.9868 | 0.8119 | 0.9186
 | ResNet18 | 0.4301 | 0.5907 | 0.7427 | 0.9695 | 0.4316 | 0.9959
 | ResNet34 | 0.8074 | 0.9027 | 0.9489 | 0.9916 | 0.8607 | 0.9562
UNet | DenseNet161 | 0.8669 | 0.9305 | 0.9640 | 0.9944 | 0.9121 | 0.9704
 | MobileNetV2 | 0.7541 | 0.8516 | 0.9199 | 0.9883 | 0.8159 | 0.9410
 | ResNet50 | 0.8306 | 0.8979 | 0.9462 | 0.9921 | 0.8894 | 0.9549
 | Xception | 0.8172 | 0.8912 | 0.9425 | 0.9915 | 0.8793 | 0.9530
UNet++ | MobileNetV2 | 0.7212 | 0.8229 | 0.9029 | 0.9854 | 0.8113 | 0.8957
 | ResNet34 | 0.8640 | 0.9267 | 0.9620 | 0.9941 | 0.8953 | 0.9780
 | ResNet50 | 0.8574 | 0.9131 | 0.9546 | 0.9933 | 0.9086 | 0.9579
Notes: HAW

## Slide 46
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 46
Evaluation Results – CAS Landslide dataset (Satellite)
Best Performing Models (Top-2) on CAS Landslide Dataset (Satellite Version)
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet | DenseNet161 | 0.8669 | 0.9305 | 0.9640 | 0.9944 | 0.9121 | 0.9704
UNet++ | ResNet34 | 0.8640 | 0.9267 | 0.9620 | 0.9941 | 0.8953 | 0.9780
5 Fold Cross Validation Result
Architecture | Backbone | Per-Image IoU | Dataset IoU | F1 Score | Accuracy | Recall | Precision
UNet++ | ResNet50 | 0.848454 | 0.925360 | 0.960543 | 0.994151 | 0.898619 | 0.968419
Due to large number of experiments; detailed results available at the link below.
  https://drive.google.com/drive/folders/18iRsnAT7VtB0DBpdMv1XW5m5eAI67ml3?usp=sharing
Notes: HAW

## Slide 47
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 47
Sample predictions – CAS Landslide dataset (Satellite)
Notes: HAW

## Slide 48
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 48
Deployment
After evaluation, the best performing model is exported in ONNX format.
Since, separate training is performed in three different datasets, three best performing model was exported.
The exported ONNX models are integrated into a Streamlit application.
Notes: HAW

## Slide 49
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 49
discussion
Model Performance Analysis
  High mIoU on CAS Landslide datasets (UAV: 95.19%, Satellite: 86.69%) due to high-resolution imagery and consistent annotations, surpassing benchmarks like Bijie (88.10%).
  Lower performance on Landslide4Sense (44.44% vs. 76.07% SOTA) due to multi-spectral complexity, class imbalance, and small patch size.
Streamlit application performing inference efficiently for landslide segmentation on Landslide4Sense and CAS Landslide datasets.
Notes: HAW

## Slide 50
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 50
discussion
Limitations
  Uneven data distribution and fixed pre-trained encoders reduce adaptability, causing lower performance.
  High-resolution CAS Landslide dataset caused GPU resource constraints, limiting training from scratch and further experiments.
  Because of large model size latency is little bit high on CPU.
Notes: HAW

## Slide 51
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 51
conclusion
Achieved up to 95.19% mIoU on UAV data;enabled precise post-disaster mapping.
Also, done experiments with multi-sensor datasets.
Deployed best performing model via Streamlit app.
Demonstrated potential for real-monitoring.
Notes: HAW

## Slide 52
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 04.09.2025 | Page 52
conclusion
Future Directions
  Combining the CAS Landslide(UAV+Satellite) datasets to train and experiments with one ultimate landslide segmentation model.
  For Landslide4Sense data, research on possible way to increase dataset, and training with different combination of loss function.
  Perform model compression techniques(like quantization, distillation) to improve latency.
Notes: HAW

## Slide 53
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 53
Notes: HAW

## Slide 54
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 54
Notes: HAW