## Slide 1: AI-POWERED LANDSLIDE REGION MAPPING USING SEMANTIC SEGMENTATION
Suraj Karki
25.08.2025
Dr.-Ing. Constanze Schwan
Notes: HAW

## Slide 2
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Introduction
Landslides are one of the most common and dangerous natural disasters globally
It causes significant damage to infrastructure, agriculture, and human life
According to the UNDRR, over 4,000 people die each year globally due to landslides 1
Rapid post-disaster mapping is vital for guiding rescue efforts and risk assessment
1. UNDRR, Human Cost of Disasters: An Overview of the Last 20 Years (2000–2019), United Nations Office for Disaster Risk Reduction, 2020. [Online]. Available: https://www.undrr.org/publication/human-cost-disasters-overview-last-20-years-2000-2019
Notes: HAW

## Slide 3
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Problem statement
Manual mapping of landslide areas in post landslide assessment is slow, inconsistent, and risky.
Precise, up-to-date landslide masks are needed for:
  Damage assessment
  Recovery planning
  Updating geohazards maps
A system is required to automatically generate post-landslide maps
Notes: HAW

## Slide 4
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
objective
To develop a deep learning model for precise landslide mapping
To obtain high performance in segmenting landslide regions from satellite and UAV imagery
To enable real-time monitoring and support disaster management efforts
Figure Source: Zhao et al. (2023), A global dataset of landslide inventories compiled from satellite imagery. Scientific Data. https://doi.org/10.1038/s41597-023-02847-z
Notes: HAW

## Slide 5
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
State of the art
Points
  Sub-points
Notes: HAW

## Slide 6
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data acquisition
Landslide4Sense Dataset
  Source: Institute of Advanced Research in Artificial Intelligence (IARAI)
  Regions: Collected from four regions (Iburi, Kodagu, Rasuwa, Taitung)
  Include earthquake and rainfall triggers landslide
  Satellite: Sentinel-2
  Topographic: ALOS (Advanced Land Observing Satellite
  Acquisition Process: Data aggregated from public satellite archives
  Annotation Process: annotations via Object-Based Image Analysis (OBIA)
Source: O. Ghorbanzadeh et al., "Landslide4Sense: Reference benchmark data and deep learning models for landslide detection," IEEE Trans. Geosci. Remote Sens., vol. 60, pp. 1–17, 2022, doi: 10.1109/TGRS.2022.3215209.
Notes: HAW

## Slide 7
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data acquisition
Landslide4Sense Dataset
Figure Source: O. Ghorbanzadeh et al., "Landslide4Sense: Reference benchmark data and deep learning models for landslide detection," IEEE Trans. Geosci. Remote Sens., vol. 60, pp. 1–17, 2022, doi: 10.1109/TGRS.2022.3215209.
Notes: HAW

## Slide 8
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data acquisition
CAS Landslide Dataset
  Source: Institute of Mountain Hazards and Environment, Chinese Academy of Sciences.
  Regions: Collected from nine diverse region
  Include earthquake and rainfall triggers landslide
  Satellite: Sentinel-2, Landsat, WorldView2/3, Planet, SuperView-1, GF-1
  UAV: High-resolution imagery from Sichuan Geomatics Center and partners.
  Acquisition Process: Satellite data sourced via Google Earth Engine, Digital Globe, and authorized providers; UAV data collected through drone
Source: Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Notes: HAW

## Slide 9
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data acquisition
Annotation Process
  Pixel-level annotations created using QGIS and LabelMe
  guided by landslide inventories, verified by geologists, cross-checked by team
Figure Source: Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Notes: HAW

## Slide 10
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
Landslide4Sense Dataset
  Total Input: 3,799 images (128x128 pixels, 14 channels).
  Channels: 12 Sentinel-2 bands (B1–B12), ALOS PALSAR slope (B13), DEM (B14).
  Output: 128x128x1 binary mask
  Split:
    Training: 3,799, Validation: 245, Testing: 800
  Distribution:
    Train Set: 2,231 landslide, 1,568 non-landslide;
    Valid Set: 146 landslide, 99 non-landslide;
    Test Set: Test: 536 landslide, 264 non-landslide.
Notes: HAW

## Slide 11
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
Bands
Notes: HAW

## Slide 12
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
Landslide4Sense Dataset
  Band Statistics:
Notes: HAW

## Slide 13
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
CAS Landslide Dataset
  Set 1: UAV
    Total Inputs: 10,939 images (512x512 pixels, 3 channels)
    Channels: RGB
    Output: 512x512x1 binary mask
  Split:
    Training: 8,753, Validation: 1093, Testing: 1093
  Distribution
    All images have landslide region
Notes: HAW

## Slide 14
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
CAS Landslide Dataset
  Set 2: Satellite
    Total Inputs: 7,422 images (512x512 pixels, 3 channels)
    Channels: RGB
    Output: 512x512x1 binary mask
  Split:
    Training: 5,938, Validation: 742, Testing: 742
  Distribution
    All images have landslide region
Notes: HAW

## Slide 15
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
UAV Data:
Subdataset | Amount | Acquisition Time | Source | Sensor | Ground Resolution (m)
Moxitaidi | 984 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 0.6
Moxitaidi | 483 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 1
Moxi Town | 1635 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 0.2
Moxi Town | 160 | 2022.09–2022.10 | Sichuan Geomatics Center | UAV | 1
Longxi River | 2504 | 2011.03–2011.05 | Sichuan Geomatics Center | UAV | 0.5
Jiuzhai Valley | 5925 | 2017.08–2017.09 | Sichuan Geomatics Center | UAV | 0.2
Jiuzhai Valley | 1752 | 2017.08–2017.09 | Sichuan Geomatics Center | UAV | 0.5
Notes: HAW

## Slide 16
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
Satellite Data:
Subdataset | Amount | Acquisition Time | Source | Sensor | Ground Resolution (m)
Palu | 817 | 2021.01–2021.11 | Digital Globe Open Data Program | WorldView2/3 | 5
Lombok | 436 | 2019.05–2019.12 | Digital Globe Open Data Program | WorldView2/3 | 5
Hokkaido Iburi-Tobu | 1484 | 2018.09–2018.10 | Geospatial Information Authority of Japan | SAT | 3
Tiburon Peninsula (Sentinel) | 606 | 2020.03–2020.06 | European Space Agency | Sentinel-2/L2A | 5
Tiburon Peninsula (Planet) | 325 | 2021.09–2021.12 | Planet | Planet | 4
Mengdong | 1155 | 2018.11.04 | Beijing Lanyu Fangyuan Technology Co., Ltd. | SuperView-1 | 0.5
Moxitaidi (SAT) | 652 | 2022.09–2022.10 | European Space Agency | Sentinel-2/L2A | 0.6
Longxi River (SAT) | 1769 | 2015.03–2015.12 | China Centre for Resources Satellite Data and Application | GF-1 | 0.5
Wenchuan | 178 | 2008.11–2008.12 | U.S. Geological Survey | Landsat | 5
Notes: HAW

## Slide 17
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Data structure
Figure Source: Y. Xu, C. Ouyang, Q. Xu, D. Wang, B. Zhao, and Y. Luo, "CAS Landslide Dataset: A large-scale and multisensor dataset for deep learning-based landslide detection," Sci. Data, vol. 11, no. 12, Jan. 2024, Art. no. 12, doi: 10.1038/s41597-023-02847-z.
Notes: HAW

## Slide 18
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
1. Unet
  A FCN originally designed for biomedical image segmentation.
  Widely used in remote sensing for image classification and
  object detection, including landslide detection
  Encoder: Captures low-level features
  Decoder: Captures high-level features and reconstructs image
  Skip Connections: preserve fine-grained details and improve
  accuracy.
Source: O. Ronneberger, P. Fischer, and T. Brox, “U-Net: Convolutional networks for biomedical image segmentation,” in Proc. Int. Conf. Med.
Image Comput.-Assist. Intervent. Cham, Switzerland: Springer, 2015, pp. 234–241.
Notes: HAW

## Slide 19
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
2. Unet++
  An improved version of U-Net
  redesigned skip pathways (shown in green): bridges the
  semantic gap between encoder and decoder
  dense skip connections (shown in blue)
  deep supervision (shown in red): allows pruning to trade off speed and accuracy by using multiple output branches.
  Enhances feature fusion for improved accuracy and gradient flow.
Source: https://jinglescode.github.io/2019/12/02/biomedical-image-segmentation-u-net-nested/
Notes: HAW

## Slide 20
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
3. PSPNet
  Uses pyramid pooling to learn global context information
  Applies regional aggregation to capture multi-scale
  features
  Fuses features from four different pyramid scales
  Achieves effective multi-scale feature learning
  Can able to efficiently work with variable size objects of the image
Source: H. Zhao, J. Shi, X. Qi, X. Wang and J. Jia, "Pyramid Scene Parsing Network," 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR), Honolulu, HI, USA, 2017, pp. 6230-6239, doi: 10.1109/CVPR.2017.660.
Notes: HAW

## Slide 21
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
4. FPN
  Designed for multi-scale segmentation
  Builds a top-down feature pyramid from deep to shallow
  layers
  Combines low-resolution semantic-rich features
  with high-resolution spatial-rich features
  Enhances segmentation of small, medium, and large objects
Source: Wangiyana, Sandhi & Samczynski, Piotr & Gromek, Artur. (2022). Data Augmentation for Building Footprint Segmentation in SAR Images: An Empirical Study. Remote Sensing. 14. 2012. 10.3390/rs14092012.
Notes: HAW

## Slide 22
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
5. MANet
  Focuses on fine-grained semantic segmentation
  Utilizes multi-scale feature extraction for diverse
  object sizes
  Incorporates attention mechanisms to highlight
  important regions
  Enhances boundary details and small object recognition
  Suitable for complex and cluttered scenes like satellite images
Source: R. Li, S. Zheng, C. Zhang, C. Duan, J. Su, L. Wang, and P. M. Atkinson, “Multiattention Network for Semantic Segmentation of Fine-Resolution Remote Sensing Images,” IEEE Transactions on Geoscience and Remote Sensing, vol. 60, pp. 1–13, 2022, doi: 10.1109/TGRS.2021.3093977.
Notes: HAW

## Slide 23
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
ML models
6. Segformer
  Transformer-based architecture for semantic segmentation
  Hierarchical Transformer encoder: extract coarse
  and fine features
  Lightweight MLP decoder: directly fuse these multi-level
  features and predict the semantic segmentation mask
  Achieves strong accuracy–efficiency trade-off for high-resolution images
  FFN: Feed-forward Network
Source: E. Xie, W. Wang, Z. Yu, A. Anandkumar, J. M. Alvarez, and P. Luo, “SegFormer: Simple and Efficient Design for Semantic Segmentation with Transformers,” arXiv preprint arXiv:2105.15203, 2021. [Online]. Available: https://arxiv.org/abs/2105.15203
Notes: HAW

## Slide 24
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
fine-tuning
Points
  Sub-points
Notes: HAW

## Slide 25
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
results
Points
  Sub-points
Notes: HAW

## Slide 26
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
discussion
Points
  Sub-points
Notes: HAW

## Slide 27
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
conclusion
Points
  Sub-points
Notes: HAW

## Slide 28
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Notes: HAW

## Slide 29
AI-Powered Landslide Region Mapping using Semantic Segmentation | Hochschule Bielefeld | 25.08.2025 | Page 2
Notes: HAW